## Slide 1: Real Time Systems Applications
RELIABILITY AND FAULT TOLERANCE
Course Coordinator: Dr. Salama A Mostafa
Address: FSKTM, 4th floor, Room No. 10
Email: salama@uthm.edu.my
Course Code: BIE 33303

## Slide 2: Reliability

## Slide 3: Reliability
Reliability is the probability of failure-free operation of a computer program for a specified period in a specified environment.
Reliability is a customer-oriented view of software quality. It relates to operation rather than design of the program, and hence it is dynamic rather than static.
The complexity of a system is inversely associated with software reliability, it is directly related to other vital factors in software quality, especially functionality, capability, etc.

## Slide 4: Reliability
Reliability is hard to achieve because the complexity of RTS turn to be high. While any system with a high degree of complexity, containing software, will be hard to reach a certain level of reliability, system developers tend to push complexity into the software layer, with the speedy growth of system size and ease of doing so by upgrading the software.
Large next-generation aircraft will have over 1 million source lines of software on-board; next-generation air traffic control systems will contain between one and two million lines; the upcoming International Space Station will have over two million lines on-board and over 10 million lines of ground support software; several significant life-critical defense systems will have over 5 million source lines of software.

## Slide 5: Reliability
RTS Major Reliability Issues
    Low failure rate
    Leads to fault tolerance design
    Gracefully degradable

## Slide 6: Failures, errors, faults
Fault – defects that cause malfunction
  Hardware fault e.g. broken wire, stuck logic
  Software fault e.g. bug
Error – unintended state caused by fault. E.g. software bug leads to wrong calculation  wrong output
Failure – errors leads to system failure (operates differently from intended)

## Slide 7: Fault
Component defects
  Depends on device
  Electronic components can have defects from manufacturing, and wear and tear.

## Slide 8: Faults
Operating environment
  Stresses
  Temperatures
  Moisture
  Vibration

## Slide 9: Classifications of faults
Nature
  By chance – broken wire
  Intentional – virus
Perception
  Physical
  Design
Boundary
  Internal – component breakdown
  External – EMI causes faults

## Slide 10: Classifications of faults
Origin
  Development e.g. in program or device
  Operation e.g. user entering wrong input
Persistence
  Transient – glitches caused by lightning
  Permanent faults that need repair

## Slide 11: Errors
Errors in specification or design
  Probably the hardest to detect
  Embedded system development:
    Specification
    Design
    Implementation
  If specification is wrong, the following steps will be wrong. E.g. unit compatibility of rocket example.

## Slide 12: Types of errors
Transient
  Regularly occurs. E.g. electrical glitches causes temporary value error
Permanent
  Transient fault can be kept in database, making it permanent.

## Slide 13: Failures
Failures can occur because of a hardware failure or a severe software issue, causing the system to freeze, reboot, or stop functioning altogether
Causes of Failures
  Errors in specification or design
  Component defects
  Environmental effects

## Slide 14: Classification of failures
Nature
  Value – incorrect output
  Timing – correct output but too late.
Perception – as seen by users
  Persistent – all users see same results. E.g. sensor reading stuck at ‘0’
  Inconsistent – users see differently. E.g. sensor reading floats (say between 1-3V, and could be seen as ‘1’ or ‘0’).
    Called malicious or Byzantine failures

## Slide 15: Classification of failures
Effects
  Benign – not serious e.g. broken tv
  Malign – serious e.g. plane crash
Oftenness
  Permanent – broken equipment
  Transient – lose wire, processors under stress (EMI, power supply, radiation)
  Transient occurs a lot more often!

## Slide 16: Example of transient failure
From report on fire control radar of F-16 fighters [3]
  Pilot noticed malfunctions every 6 hrs
  Pilot requested maintenance every 31 hrs
  1/3 of requests can be reproduced in workshop
  Overall less than 10% of transient failures can be reproduced!

## Slide 17: Definitions
Reliability R(t)
  Probability that a system will perform its intended function in the specified environment up to time t.
Maintainability M(t)
  Probability that a system can be restored within t units after a failure.
Availability A(t)
  Probability that a system is available to perform the specified service at tdt. (% of system working)

## Slide 18: Reliability
R(0) = 1, R(
Failure density f(t) = -dR(t)/dt
Failure rate (t) = f(t)/R(t)
(t) dt is the conditional probability that a system will fail in the interval dt, provided it has been operational at the beginning of this interval
When (t) = constant then R(t) = e-t
= MTTF (Mean Time to Failure)

## Slide 19: Failure rate
(t)
Real-time
Period of constant Failure Rate
Early
faillures
Late
faillures
Burn-in
Wear-out

## Slide 20: Failure rate vs Costs [4]
(t)
Cost of System
US Air Force:
Failure rate of electronic systems
within a given technology
increases with increasing system cost.

## Slide 21: Maintainability
Measured by Repair-rate 
When (t) = constant then M(t) = e-t
= MTTR (Mean Time to Repair)
Preventive maintenance:
  If  increases in time, then it makes sense to replace the aging unit.
  If  of different units evolves differently, preventive maintenance consists in replacing the “Smallest Replaceable Units” with growing 

## Slide 22: Reliability vs. Maintainability
Reliability and maintainability are, to a certain extent, conflicting goals.
Example: Connectors
Inside a SRU, reliability must be optimized
Between SRU’s, maintainability is important
Plug
Solder
Reliability
bad
good
Maintainability
good
bad

## Slide 23: Availability
A = MTTF / ( MTTF + MTTR )
Good availability can be achieved either
  by a high MTTF
  by a small MTTR
A high system MTTF can be achieved by means of fault tolerance: the system continues to operate properly even when some components have failed.
Fault tolerance reduces also the MTTR requirements.

## Slide 24: Fault Tolerance
Fault tolerance is a process that enables an operating system to respond to a failure in hardware or software
Fault tolerance is obtained through redundancy (more resources assigned to a task than strictly required)
Redundancy can be used for
    Fault detection
    Fault correction
Redundancy can be implemented at various levels
    at component level
    at processor level
    at system level

## Slide 25: Redundancy in components
Error detection
  to correct transient errors by retry
  to avoid using corrupted data
Error correction
  to correct transient errors on the fly
  to remain operational after catastrophic component failure
  Scheduled maintenance instead of urgent repair.

## Slide 26: Fault detection at Processor Level
C
P
U
1
C
P
U
2
=
Error

## Slide 27: Fault correction at Processor Level
C
P
U
1
C
P
U
3
C
P
U
2
Voting Logic

## Slide 28: Replica Determinism
A set of replicated RT objects is “replica determinate” if all objects of this set visit the same state at about the same time.
“At about the same time” makes a concession to the finite precision of the clock synchronization
Replica determinism is needed for
  consistent distributed actions
  fault tolerance by active redundancy
Lack of replica determinism makes voting meaningless.
Example: Airplane on takeoff
System 1:
System 2:
System 3:
Majority:
Take off
Abort
Take off
Take off
Accelerate Engine
Stop Engine
Stop Engine (fault)
Stop Engine

## Slide 29: Fault Correction at System Level
S
Y
S
T
E
M
1
S
Y
S
T
E
M
2
Error Detection
Hot Stand-By
  systems continue to work, uninterrupted,
  when one or more of its hardware
  components fail.

## Slide 30: Fault Correction at System Level
S
Y
S
T
E
M
1
S
Y
S
T
E
M
2
Error Detection
Common Memory
Cold Stand-By
  a redundancy of having one
  system as a backup for another
  identical primary system

## Slide 31: Fault Correction at System Level
S
Y
S
T
E
M
1
S
Y
S
T
E
M
2
Distributed Common Memory
Error Detection
Distributed Common Memory
  Each processor has access to the memory of the other
  Each processor keeps a copy of all critical processes

## Slide 32: Fault Correction at System Level
Common Memory
S
Y
S
T
E
M
1
S
Y
S
T
E
M
1
S
Y
S
T
E
M
1
S
Y
S
T
E
M
1
Load Sharing

## Slide 33: Safety Critical systems
S
Y
S
1
Voting Logic
S
Y
S
2
S
Y
S
4
S
Y
S
3
Fail once, still operational
Fail twice, still safe

## Slide 34: Safety Critical Systems
S
Y
S
1
Voting Logic
S
Y
S
2
S
Y
S
4
S
Y
S
3
S
Y
S
5
Space Shuttle Computer system
in case of a Software Bug

## Slide 35: Failure and Damage

## Slide 36: Damage
Physical damage means destruction of devices and other hardware
Damage could be a result from equipment failure, software corruption, sabotage, or occasionally be from human error and could leave the system unable to function.
Failure characterizes lack of functioning sometimes due to damage materials or parts.

## Slide 37: Damage Confinement and Assessment
Fault treatment and continued service — an error is a symptom of a fault; although the damage is repaired, the fault may still exist
Damage assessment is closely related to damage confinement techniques used
Damage confinement is concerned with structuring the system so as to minimize the damage caused by a faulty component (also known as firewalling)
Modular decomposition provides static damage confinement; allows data to flow through well-define pathways (assuming strongly type language)
Atomic actions provides dynamic damage confinement. They are used to move the system from one consistent state to another

## Slide 38: Thank You
Real Time Systems Applications